## Slide 1: EMBEDDED AI: ROAD OBJECT DETECTION
Embedded AI (tinyML) for road object detection
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev
Source https://www.anolytics.ai/blog/use-of-bounding-box-annotations-is-important-for-object-detection/

## Slide 2: EMBEDDED AI: ROAD OBJECT DETECTION
The Problem
Traditional AI requires a lot of computing power. To perform object detection today, most systems rely on power-hungry GPUs or expensive cloud latency. This is a deal-breaker for edge cloud for smart cities, remote monitoring, and battery-operated IoT.
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev
The Value Proposition
Embedded machine learning has emerged as an effective approach for enabling intelligent perception on low-power devices with limited memory and computational capacity

## Slide 3: EMBEDDED AI: ROAD OBJECT DETECTION
Hardware
Software and Engineering for Embedded Systems
Development board with camera sensor
LCD screen

## Slide 4: EMBEDDED AI: ROAD OBJECT DETECTION
Software and Engineering for Embedded Systems

## Slide 5: EMBEDDED AI: ROAD OBJECT DETECTION
Software and Engineering for Embedded Systems
AI Model Selection
Criteria | FOMO MobileNetV2 | MobileNet SSD | YOLOv5n / Tiny-YOLO | Single-label MobileNetV1 | 
Latency on ESP32-S3 | ~140–200 ms (~5–10 FPS) | ~800 ms+ (~1 FPS) | several seconds/frame | ~100 ms (~10 FPS) | 
RAM footprint | < 200 KB | 1 MB, needs PSRAM | > 2 MB | < 100 KB | 
Output type | Object centroids + class | Bounding boxes + class | Bounding boxes + class | Single class | 
Multi-object localization | yes | yes | yes | no | 
Size estimation | no | yes | yes | no | 
ESP-NN / TFLite Micro support | Full (Edge Impulse) | Partial (slow ops) | Requires custom porting | Full | 
Training pipeline | Mature (Edge Impulse Studio) | Mature but heavier | mature but heaviest | Trivial | 
Selection of model | Selected | Dropped - latency, RAM | Dropped - infeasible on MCU | Option - no localization | 
We have studied below options in depth. Given limitations of the MCU,

## Slide 6: EMBEDDED AI: ROAD OBJECT DETECTION
Software and Engineering for Embedded Systems
FOMO object detection performance test with ESP32-S3 result
Set variables:
Input resolution (e.g. 96×96 grayscale)
Heatmap factor: 8. # of epochs: Learning rate: 0.001
Augmentation pipeline: INT8 quantization:
Classes: Car, Bus, Truck, Bicycle, Motorcycle

## Slide 7: EMBEDDED AI: ROAD OBJECT DETECTION
Software and Engineering for Embedded System
How to improve performance drop with higher number of classes with given MCU?
Stage 1
PIR
Active : ~0.3 mW
MCU 1
Active : ~200-300 mW
D. Sleep: ~0.4 mW
Stage 2
Stage 3
ToF
Camera
MCU 2
WiFi interrupt
MCU 3,4,5, 6…
Car /
Others
Bus
/ Others
Truck
/Others
8 x 8 matrix POI zones
Object detected
Wake up MCU 1
Wake up MCU 2
Return to deep sleep MCU 1
ToF sensor on
Camera takes shot
MCU 2 makes 1st classification (Bus)
Wake up MCU 4 (Bus)
Send picture data to MCU 4
Return to deep sleep MCU 2
Inference (binary classification) for final confirmation
If result below 80% , wake up MCU 5
Send picture data to MCU 5
Inference and output highest score class
(bus or truck)
WiFi
interrupt
Bicycle
/Others
In order to achieve production level classification & energy capability, we would like to propose a hybrid
deterministic and AI solution in multiple stages. Below system is composed of PIR sensor to wake up all system
from deep sleep state when an object detected, multi-zone ToF (Time of Flight) sensor for initial deterministic
Classification and finally camera sensor and multi-MCUs for binary AI classification; given the fact that binary AI
classification gave the highest score during tests.

## Slide 8: EMBEDDED AI: ROAD OBJECT DETECTION
Software and Engineering for Embedded System
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.5 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.8 | 0.7 | 0.6 | 0.3 | 0.1 | 0.1 | 0.1 | 0.1
0.7 | 0.8 | 0.9 | 0.7 | 0.1 | 0.1 | 0.1 | 0.1
0.6 | 0.7 | 0.5 | 0.7 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
0.1 | 0.1 | 2.1 | 1.5 | 1.7 | 1.9 | 0.1 | 0.1
0.1 | 1.6 | 2.9 | 2.5 | 2.6 | 2.6 | 0.1 | 0.1
0.8 | 1.9 | 2.9 | 2.9 | 2.9 | 2.9 | 0.1 | 0.1
0.7 | 0.8 | 2.9 | 2.9 | 2.9 | 2.9 | 0.1 | 0.1
0.6 | 0.7 | 1.6 | 0.7 | 0.1 | 1.6 | 0.1 | 0.1
Speed : 50 kmh
Usual scene
Speed : 1.5 m x 2.5 m
 Car
How to use ToF sensor for deterministic classification?
Range 4 – 10 m

## Slide 9: EMBEDDED AI: ROAD OBJECT DETECTION
FOMO (Faster Objects, More Objects) MobileNet – What it is and Advantages
Conventional object detection methods attempt to predict bounding boxes by estimating the precise width and height of each object, a process that imposes considerable computational and memory overhead. FOMO reduces this burden by simplifying assumptions
Why it’s preferred for the ESP32-S3
Speed: FOMO is roughly 30x faster than MobileNet SSD. On the ESP32-S3, you can achieve 10–20 frames per second, whereas YOLO might take several seconds per frame.
Memory: It can run in less than 200KB of RAM. Since the ESP32-S3 has 512KB, this leaves plenty of room for your camera buffer and other code logic.
Counting: Because it works on a grid, it is naturally very good at counting many objects (like multiple cars in a parking lot) without needing the complex "Non-Maximum Suppression" math that YOLO requires.
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev

## Slide 10: EMBEDDED AI: ROAD OBJECT DETECTION
FOMO (Faster Objects, More Objects) MobileNet - Drawbacks
The advantages are achieved at the cost of several limitations.
No Size Detection: FOMO won't tell if a car is "large" or "small" in the frame. It assumes all objects are roughly the same size as the grid cells.
Minimum Distance: If two objects are so close that their centers fall into the same grid cell, FOMO will only count them as one object.
Square Assumption: FOMO works best when objects are somewhat square or circular. Extremely long, thin objects can sometimes confuse the grid.
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev

## Slide 11: EMBEDDED AI: ROAD OBJECT DETECTION
TensorFlow Lite for Microcontrollers (TFLM)
Standard TFLite Micro is an interpreter-based runtime. When ESP32 boots up, TFLite allocates a chunk of RAM (aka the tensor arena), loads the model dynamically from a .tflite flatbuffer file, parses the model graph at runtime, and maps out how to route data through the layers.
The interpreter itself takes up valuable Flash space, and the generic graph overhead eats up RAM.
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev

## Slide 12: EMBEDDED AI: ROAD OBJECT DETECTION
TensorFlow Lite for Microcontrollers (TFLM)
Standard TFLite Micro is an interpreter-based runtime. When ESP32 boots up, TFLite allocates a chunk of RAM (aka the tensor arena), loads the model dynamically from a .tflite flatbuffer file, parses the model graph at runtime, and maps out how to route data through the layers.
The interpreter itself takes up valuable Flash space, and the generic graph overhead eats up RAM.
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev

## Slide 13: EMBEDDED AI: ROAD OBJECT DETECTION
Conclusion
By combining curated vehicle datasets, Edge Impulse’s FOMO architecture, grayscale preprocessing, and embedded-oriented optimization strategies, the Embedded ML object detection offers
Real-Time Responsiveness (Ultra-Low Latency) for edge cloud and IoT: Processing happens at the source not at the central cloud
Cost Efficiency: Battery-powered low cost MCUs reports "Spot Occupied" or "Spot Empty" using local inference, instead of expensive, high-speed cameras wired to a central computer
Privacy and Data Security : Sensitive information stays on site instead of sending to central cloud.
Extreme Power Longevity: Many real-world sensors are placed in locations where they cannot be plugged into a wall
Bandwidth Independence : The device operates fully offline. No need to upload heavy image files to perform its task. A vehicle counter on a remote bridge to monitor structural load, can log traffic data for months and only sync the final "count" once a month via a low-bandwidth connection
Software and Engineering for Embedded Systems
Deniz Dag & Murat Kezlev